## Slide 1: Scalable SA

## Slide 2: Goals
Scale Infiniband to tens of thousands of nodes
Distribute needed subnet data to end nodes
  Example: provide path records to compute nodes for connection establishment
Collect and redistribute data and events
  Example: name and address resolution services
  Example: error detection and reporting
Provide fault tolerance

## Slide 3: Conceptual Overview
Designed for scalability
  Reduce load on centralized SA
  Allow for saving / restoring data from disk
  Parallel access (lockless) to data
Nodes join a data distribution tree
  Not necessarily binary
SA data is pushed down the tree
Events are reported up the tree

## Slide 4: Architecture
Divided into 4 functional layers
Subnet data is communicated up/down a distribution tree
Failover communication built into protocol

## Slide 5: Core Layer
Overall management of SSA data and members
  Subnet data is encapsulated into specific databases
  Members request access to a database
  Databases filter SA data for scalability and security purposes
Manages SSA memberships
  Tracks which nodes have joined a data distribution tree and their location in the tree
  Rebalances tree as nodes join/leave

## Slide 6: Core Layer
Handles error recovery
  Assigns backup nodes to handle failures
  Receives and responds to error events
Extracts raw data from SA
Translates raw data into SSA databases
  Raw data not suitable for transmitting over the network (pointers, byte ordering, locking, etc.)

## Slide 7: Distribution Layer
Communicates data between SSA members
Pushes SSA database down distribution tree
Processes database tables and updates
Is mostly data agnostic
  Table definitions are generic

## Slide 8: Access Layer
Formats SSA data for consumer use
Extracts required consumer data from database tables
Handles higher level queries to extract SA attributes
  Example: path record from name

## Slide 9: Consumer
End nodes for compute, storage, etc.
Requires minimal to zero impact on applications
SSA designed to minimize impact to node during job execution

## Slide 10: SSA Database
Collection of tables and their definitions
  Modeled after relational databases
  Is not a RDMS
    No primary/foreign keys, indices, etc.
Handles incremental updates
  Changes to database move from one consistent state to another
  Each set of changes tracked as a single transaction
  Transaction log used to publish and process updates

## Slide 11: Table Definition
Name of table
Type of table
  Data or transaction log
Size of records
  Fixed or variable sized
Size and location of fields
  Primarily for debugging and logging
Definition version

## Slide 12: Database Tables
Array of data records
Tables may be explicitly related
  Linking a table with fixed sized records to a variable sized data
  Linking tables based on data is outside of database definitions
Changes to data captured in transaction log

## Slide 13: Epoch Number
Versioning for the data
As data is modified, the epoch number is incremented
Allows clients to determine if they have the latest data
  Indicates how many updates are needed to bring the data back into sync

## Slide 14: Transaction Log
Stores incremental update information
Each transaction is associated with a specific epoch number
Allows clients to roll changes forward or back
  Roll forward to update local database
  Roll back to obtain a consistent snapshot of data while changes are being applied
    For lockless access to database

## Slide 15: Implementation
3 daemons
SA plugin
  Core, distribution, and access layers
SSA daemon
  Distribution and access layers
IB ACM
  Consumer

## Slide 16: Management Communication
Management done over QP1
Core reachable at SM LID
Application specific MAD class
Join / leave requests
Set parent(s) for distribution tree

## Slide 17: Data Communication
Data exchanges over rsockets
  Connected QPs with RDMA write capability
  Keep-alive support for failure detection
Data flows node to node up/down tree
Extensible protocol used for database transfers
  Allow for future data sets
Consumer specific protocol to access layer

## Slide 18: Thread Model
Main control thread
  Processes local events (port up/down), handles management traffic, listens for downstream clients
Upstream communication thread
  Connects up tree, processes database updates
Downstream communication threads
  Connect down tree, notifies clients of data changes
  One downstream thread can handle multiple clients
Communication between local threads uses socketpairs

## Slide 19: Data Protocol Details
Upstream thread connects to parent
  Parent assigns connection to one of its downstream thread
Requests database table definitions
For each definition, requests table data
Parent notifies child when updates occur
Child pulls updated transaction log
Transaction log changes can be pushed down tree before updates are applied to the local database

## Slide 20: Transaction Log Processing
Log is comprised of multiple tables
  Records which <table, record> has changed
  Includes both new and old data
Upstream thread writes new epoch value for record
Record is replaced
Once all records have been updated, epoch value for database is updated

## Slide 21: Transaction Log Processing
Downstream thread reads database epoch value
  All generated data will align with this epoch
Desired record is read
Reads record epoch value
If epochs differ, desired record must be found in the transaction log

## Slide 22: Consumer Protocol Details
Consumer publishes RDMA write target buffer
  Buffer stores upstream database epoch value
Parent writes to epoch buffer on change
Consumer checks for changes when convenient
  Usually when establishing new connections
  Avoids pulling updates during job execution
Consumer integrates changes into local cache